## Slide 1
DDCA PROJECT · DEPARTMENT OF CSE
4-Bit XOR-Based Data Encryption & Decryption Unit
Design and simulation of a purely combinational, gate-level symmetric-key cipher in Logisim
PRESENTED BY
Shreyesh Reddy Gudi
2620030608
Kaustubha Srinivas Kaseebhotla
2620030601
Rachuri Harshita
2620030654
Rudrakashala Harshitha
2620030591
Guide: Kartheek B.Tech CSE · Batch-10 · AY 2026–2030 KL University, Hyderabad

## Slide 2
Introduction
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
02 / 14
Background
Cryptography secures digital data. XOR is a fundamental building block of many ciphers because it is perfectly reversible.
Domain
Digital Logic Design & Data Security — bitwise encryption and decryption implemented at the gate level and simulated in Logisim.
Why it matters
Hardware-level encryption underpins secure embedded systems and the foundations of stream ciphers — turning Boolean algebra into a working circuit.
CORE ELEMENT
XOR gate ( ⊕ )
CIRCUIT TYPE
Purely combinational
(no clock, no memory)
DATA WIDTH
4-bit plaintext + 4-bit key
TOOL
Logisim simulation

## Slide 3
Problem Statement
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
03 / 14
The need: a simple, educational hardware implementation of symmetric encryption — the same key to encrypt and decrypt — built only from basic logic components, without complex algorithms or software libraries.
LIMITATIONS OF EXISTING APPROACHES
Software-only demos
Hide gate-level hardware behaviour behind code and libraries.
Complex ciphers (AES, DES)
Far too complex to design, wire and explain within an undergraduate lab.
Incomplete student circuits
Focus on physical security or encryption alone — no reversible decryption or verification logic.

## Slide 4
Literature Survey / Existing Systems
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
04 / 14
Approach | How it works | Limitation
Software XOR ciphers | XOR applied in program code | Easy to write, but offers no hardware insight
Block ciphers (AES, DES, Blowfish) | Complex multi-round algorithms | High gate count; not feasible to hand-wire in a lab
LFSR stream ciphers | Shift registers generate a pseudo-random key-stream | Needs flip-flops, memory and a clock
Access-control projects (RFID / keypad) | Compare an entered code with a stored value | Secure physical entry only — the data stays unprotected
Basic gate demos (AND / OR / NOT) | Illustrate individual gate behaviour | Rarely show reversible crypto; no verification stage
This project | 8 XOR gates + comparators, purely combinational | Reversible, self-verifying and lab-friendly

## Slide 5
Objectives
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
05 / 14
01
Encrypt
Build a 4-bit XOR encryptor:
C = P ⊕ K
02
Decrypt
Recover the plaintext with the same key:
D = C ⊕ K
03
Verify
Comparators confirm the output automatically:
D == P
04
Simulate
Build and test the complete circuit in
Logisim
05
Document
Validate with truth tables for
1-bit & 4-bit cases
Design constraint: gates and comparators only — no encoders, decoders or memory elements.

## Slide 6
Proposed System
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
06 / 14
THE CORE IDENTITY
(P ⊕ K) ⊕ K = P
XOR is its own inverse, so one shared key both encrypts and decrypts — with perfect recovery of the original plaintext.
A complete 4-bit symmetric encryption–decryption system built from XOR gates and comparators.
Pure combinational
8 single-bit XOR gates — no clock and no memory anywhere.
One shared key
The same key lines drive both the encryption and decryption stages.
Built-in self-check
Comparators confirm Decrypted == Plaintext for every test vector.
Modular & scalable
Bit-level stages C0–C3 and D0–D3; extendable to 8/16-bit designs.

## Slide 7
System Architecture
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
07 / 14
PLAINTEXT
P3 – P0
XOR ENCRYPT
C = P ⊕ K
CIPHERTEXT
C3 – C0
XOR DECRYPT
D = C ⊕ K
DECRYPTED
D3 – D0
KEY K3 – K0
same key reused
COMPARATOR
MATCH = 1 if D = P
original plaintext (reference for verification)
Key insight: XOR is its own inverse → (P ⊕ K) ⊕ K = P

## Slide 8
Methodology / Implementation
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
08 / 14
1
Define inputs
Pins P0–P3 (plaintext) and K0–K3 (key)
2
Encrypt
Four XOR gates: C0 = P0⊕K0 … C3 = P3⊕K3
3
Decrypt
Four more XOR gates reuse the same key lines
4
Verify
Comparators check each decrypted bit against its plaintext bit
5
Simulate
Poke P and K live; D always equals P
CORE LOGIC EQUATIONS
Ci = Pi ⊕ Ki
Di = Ci ⊕ Ki = Pi
Matchi = (Di == Pi)
Tools: Logisim — Wiring, Gates and Arithmetic libraries

## Slide 9
Logisim Implementation — Complete Circuit
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
09 / 14
INPUTS
ENCRYPT C0–C3
DECRYPT D0–D3
VERIFY
8
input pins
4 plaintext + 4 key
8
XOR gates
4 encrypt + 4 decrypt
4
comparators
one per bit: D vs P
0
flip-flops
no clock, no memory

## Slide 10
Bit-by-Bit Verification in Simulation
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
10 / 14
STAGE 1 Comparator on Bit 0
STAGE 2 Comparator on Bit 1
STAGE 3 Comparator on Bit 2
STAGE 4 Comparator on Bit 3
How it was verified
One bit at a time
A comparator is wired to the plaintext and decrypted line of each bit in turn.
Lit output = match
The comparator output confirms that bit survives the round trip.
Combined result
All four comparators run together in the final build (previous slide).

## Slide 11
Results — Truth Table & Test Vector
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
11 / 14
1-bit encrypt / decrypt round trip
P | K | C = P⊕K | D = C⊕K | Match
0 | 0 | 0 | 0 | ✓ Yes
0 | 1 | 1 | 0 | ✓ Yes
1 | 0 | 1 | 1 | ✓ Yes
1 | 1 | 0 | 1 | ✓ Yes
For every row, D reproduces P exactly.
Example 4-bit test vector
Plaintext P
1
0
1
1
Key K
⊕
1
1
0
0
Ciphertext C
0
1
1
1
Key K
⊕
1
1
0
0
Decrypted D
1
0
1
1
✓ D = P → MATCH

## Slide 12
Results & Discussion
DDCA Project | 4-Bit XOR Encryption & Decryption Unit
12 / 14
16 / 16
input combinations of P and K recovered perfectly
8
XOR gates form the complete cipher
4
bit-wise comparators give instant feedback
0
flip-flops, clocks or memory elements
Finding
Across every tested combination, the decrypted output D exactly reproduced the plaintext P and the MATCH output stayed high — confirming correctness at the gate level.
Limitation
An educational single-round cipher, not production-grade: reusing one key across messages would be vulnerable.

## Slide 13
Conclusion & Future Scope
WHAT WAS ACHIEVED
Designed and simulated a complete 4-bit symmetric XOR cipher in Logisim
Verified (P ⊕ K) ⊕ K = P across all tested vectors — perfect recovery
Integrated comparators for real-time correctness feedback
Documented behaviour with truth tables and worked test cases
Kept the design minimal: no encoders, decoders or memory
FUTURE SCOPE
Wider data path
Scale to 8- or 16-bit words
Pseudo-random keys
Add a key generator or key schedule
Building block
Reuse as a module in larger designs
All stated objectives were fulfilled — the circuit is ready for demonstration and further academic exploration.

## Slide 14
Thank You
Questions & Discussion
(P ⊕ K) ⊕ K = P
Shreyesh Reddy Gudi · Kaustubha Srinivas Kaseebhotla · Rachuri Harshita · Rudrakashala Harshitha
Guide: Kartheek · Computer Science and Engineering, KL University, Hyderabad